## Slide 1: Part 2
Mobile graphics trends
Hardware architectures
Applications

## Slide 2
Hardware architectures

## Slide 3: Brief history of mobile graphics hardware
2016
2015
2014
2013
2012
2011
2010
2009
2008
2007
iPhone (MBX)
Buys Imageon (Adreno)
Apple (PowerVR)
AMD
Nvidia
Qualcomm Snapdragon/Adreno
Imagination
PowerVR
Intel
Buys PA Semi
Omnia HD (TI OMAP 3 & Power VR SGX530)
Samsung
(mostly ARM)
ARM Mali
iPhone 3GS (SGX535)
A4 (ARM Cortex A8)
Hummingbird (Cortex A8)
Adreno 530 GLES 3.1+, OpenCL 2, DX 11.2 Vulcan 1.0
Plans to build its own GPU
Exynos 5433/7410 (20nm, Mali-T760 MP6)
Sells Imageon
MBX
SGX535/541 (GLES 2.0)
SGX545 (GLES 2.0 GL 3.2)
SGX543 (GLES 2.0, GL 2.1)
Furian?
Apple will no longer require its services in 18-24 months
Series 6XE/XT GLES 3.1 GL 3.2 (28nm)
Series7XE Vulkan 1.0 GLES 3.1 (latter ones 10nm)
Tegra 2 (Cortex-A9, GLES 2.0)
Tegra 3 (Cortex-A9, GLES 2.0)
Tegra 4 (Cortex-A15, GL 4.4, 28nm)
Tegra K1 (Cortex-A15, GL 4.4, 28nm)
Tegra X1 (Cortex-A57, GLES 3.1, GL 4.5, Vulkan, 20nm)
Next Tegra generations seem to be for automotive
Buys Phalanx
Mali 400 GLES 2.0
T600 GLES 2.0, DX9.0
T700 GLES 3,1, DX 11.1 OpenCL 1.1
T800 GLES 3,1, DX 11.1-11.2 OpenCL 1.2
A9 (GT7600)
A7/A8 & A8X (GT64XX)
Notes: Intel/ARM
http://www.infoworld.com/d/computer-hardware/intel-vs-arm-two-titans-tangled-fate-237265?page=0,1
AMD
http://www.anandtech.com/show/7514/amd-2014-mobile-apu-update-beema-and-mullins
http://www.enterprisetech.com/2014/05/05/amd-unify-x86-arm-systems-skybridge/

## Slide 4: Architectures (beginning 2015)
MIPS
ARM
x86
Notes: Intel/ARM
http://www.infoworld.com/d/computer-hardware/intel-vs-arm-two-titans-tangled-fate-237265?page=0,1
AMD
http://www.anandtech.com/show/7514/amd-2014-mobile-apu-update-beema-and-mullins
http://www.enterprisetech.com/2014/05/05/amd-unify-x86-arm-systems-skybridge/

## Slide 5: Architectures
x86 (CISC 32/64bit)
  Intel Atom Z3740/Z3770, X3/X5/X7
  AMD Amur / Styx (announced)
  Present in few smartphones, more common in tablets
  Less efficient
ARM
  RISC 32/64bit
    With SIMD add-ons
  Most common chip for smartphones
  More efficient & smaller area
MIPS
  RISC 32/64bit
  Including some SIMD instructions
  Acquired by Imagination, Inc. @2014
Notes: Intel/ARM
http://www.infoworld.com/d/computer-hardware/intel-vs-arm-two-titans-tangled-fate-237265?page=0,1
AMD
http://www.anandtech.com/show/7514/amd-2014-mobile-apu-update-beema-and-mullins
http://www.enterprisetech.com/2014/05/05/amd-unify-x86-arm-systems-skybridge/

## Slide 6: Architectures – RISC vs. CISC but…
CISC (Complex Instruction Set Computer)
  Fast program execution (optimized complex paths)
  Complex instructions (i.e. memory-to-memory instructions)
RISC (Reduced Instruction Set Computer)
  Fast instructions (fixed cycles per instruction)
  Simple instructions (fixed/reduced cost per instruction)
FISC (Fast Instruction Set Computer)
  Current RISC processors integrate many improvements from CISC: superscalar, branch prediction, SIMD, out-of-order
  Philosophy  fixed/reduced cycle count/instr
  Discussion (Post-RISC):
    http://archive.arstechnica.com/cpu/4q99/risc-cisc/rvc-5.html
Notes: CISC – fast program execution, complex HW
RISC – fast instructions, simple HW, complexity on the compiler
FISC – starts from RISC, takes from CISC, improve performance at the cost of HW complexity
Intel/ARM
http://www.infoworld.com/d/computer-hardware/intel-vs-arm-two-titans-tangled-fate-237265?page=0,1
AMD
http://www.anandtech.com/show/7514/amd-2014-mobile-apu-update-beema-and-mullins
http://www.enterprisetech.com/2014/05/05/amd-unify-x86-arm-systems-skybridge/

## Slide 7: Landscape has changed a bit…
Status by 2014-2015:
  Intel Atom X3/X5/X7 announced (March 2015)
  AMD announces Amur / Styx (20nm, Oct. 2014)
  Nvidia launches Tegra X1 (March 2015)
  ARM the only EU big technology company
  Imagination announces Furian (sub 14nm, March 2017) Imagination’s chips are in iPhones & iPads
Nowadays:
  Intel quits mobile Apr/May 2016
  AMD cancels 20nm chips (Jul. 2015)
  Nvidia cancels Shield tablet (Aug. 2016)
  ARM acquired by Softbank (Sep. 2016)
  Apple tells Imagination that their IP will not be needed in 18-24 months (Apr. 2017)
Notes: Intel/ARM
http://www.infoworld.com/d/computer-hardware/intel-vs-arm-two-titans-tangled-fate-237265?page=0,1
AMD
http://www.anandtech.com/show/7514/amd-2014-mobile-apu-update-beema-and-mullins
http://www.enterprisetech.com/2014/05/05/amd-unify-x86-arm-systems-skybridge/

## Slide 8: Architectures (nowadays)
MIPS
ARM
x86
Acquired by Imagination, inc
Notes: Intel/ARM
http://www.infoworld.com/d/computer-hardware/intel-vs-arm-two-titans-tangled-fate-237265?page=0,1
AMD
http://www.anandtech.com/show/7514/amd-2014-mobile-apu-update-beema-and-mullins
http://www.enterprisetech.com/2014/05/05/amd-unify-x86-arm-systems-skybridge/

## Slide 9: Architectures – ARM
ARM Ltd.
  RISC processor (32/64 bit)
  IP (intellectual property) – Instruction Set / ref. implementation
  CPU / GPU (Mali)
Licenses (instruction set OR ref. design)
  Instruction Set license -> custom made design (SnapDragon, Samsung in Galaxys, Apple in iPones & iPads)
    Optimizations (particular paths, improved core freq. control,…)
  Reference design (Cortex A9, Cortex A15, Cortex A53/A57…)
Licensees (instruction set OR ref. design)
  Apple, Qualcomm, Samsung, Nvidia, AMD, MediaTek, Amazon (through Annapurna Labs, Inc.)…
  Few IS licenses, mostly adopting reference design
Manufacturers
  Contracted by Licensees
    GlobalFoundries, United Microelectronics, TSM…

## Slide 10: Architectures – ARM…
Suppported on
  Android, iOS, Win Phone, Tizen, Firefox OS, BlackBerry, Ubuntu Phone, …
Biggest mobile market share
Typically paired with mobile GPUs. Existing brands:
  Adreno 4x0/5x0 – Qualcomm
  PowerVR 8XE (Rogue) – Imagination
  Mali T8x0/G51/G71 – ARM
General strategies:
  Cache coherence – week sequential code guarantees on multithreading!!
  Heavy dependence on compiler  optimize instruction scheduling
    Operation dependencies , loop unrolling, etc…
  Use SIMD extensions

## Slide 11: Architecture types
High performance
  Premium smartphones & tablets
High area efficiency
  Medium-to-low smartphones
Ultra-low power
  Smartwatches
Notes: Intel/ARM
http://www.infoworld.com/d/computer-hardware/intel-vs-arm-two-titans-tangled-fate-237265?page=0,1
AMD
http://www.anandtech.com/show/7514/amd-2014-mobile-apu-update-beema-and-mullins
http://www.enterprisetech.com/2014/05/05/amd-unify-x86-arm-systems-skybridge/

## Slide 12: Architectures
Mobile GPU architecture trends
Notes: Intel/ARM
http://www.infoworld.com/d/computer-hardware/intel-vs-arm-two-titans-tangled-fate-237265?page=0,1
AMD
http://www.anandtech.com/show/7514/amd-2014-mobile-apu-update-beema-and-mullins
http://www.enterprisetech.com/2014/05/05/amd-unify-x86-arm-systems-skybridge/

## Slide 13: Graphics pipeline trends
Tiled rendering
Data (texture) compression
Other optimizations
Notes: Intel/ARM
http://www.infoworld.com/d/computer-hardware/intel-vs-arm-two-titans-tangled-fate-237265?page=0,1
AMD
http://www.anandtech.com/show/7514/amd-2014-mobile-apu-update-beema-and-mullins
http://www.enterprisetech.com/2014/05/05/amd-unify-x86-arm-systems-skybridge/

## Slide 14: Tiled Rendering
Immediate Mode Rendering (IMR)
Tile-Based Rendering (TBR)
Tile-Based Deferred Rendering (TBDR)
Notes: IMR / TBR / TBDR
http://blog.imgtec.com/powervr/understanding-powervr-series5xt-powervr-tbdr-and-architecture-efficiency-part-4
http://wenku.baidu.com/view/85ea8fec998fcc22bcd10dcb.html

## Slide 15: Architectures – GPU
Inmediate Mode Rendering (IMR)
  Geometry is processed in submission order
    High overdraw (shaded pixels can be overwritten)
  Buffers are kept in System Memory
    High bandwidth / power / latency
  Early-Z helps depending on geometry sorting
    Depth buffer value closer than fragment  discard
http://blog.imgtec.com/powervr/understanding-powervr-series5xt-powervr-tbdr-and-architecture-efficiency-part-4
VS
FS
Notes: IMR / TBR / TBDR
http://blog.imgtec.com/powervr/understanding-powervr-series5xt-powervr-tbdr-and-architecture-efficiency-part-4
http://wenku.baidu.com/view/85ea8fec998fcc22bcd10dcb.html

## Slide 16: Architectures – GPU
Tile Based Rendering (TBR)
  Rasterizing per-tile (triangles in bins per tile) 16x16, 32x32
    Buffers are kept on-chip memory (GPU) – fast!  geometry limit?
  Triangles processed in submission order (TB-IMR)
    Overdraw (front-to-back -> early z cull)
  Early-Z helps depending on geometry sorting
http://blog.imgtec.com/powervr/understanding-powervr-series5xt-powervr-tbdr-and-architecture-efficiency-part-4

## Slide 17: Architectures – GPU
http://blog.imgtec.com/powervr/understanding-powervr-series5xt-powervr-tbdr-and-architecture-efficiency-part-4
Limit: ~100Ktri + complex shader
Tile Based Deferred Rendering (TBDR)
  Fragment processing (tex + shade) ~waits for Hidden Surface Removal
    Micro Depth Buffer – depth test before fragment submission
      whole tile  1 frag/pixel 
    iPAD 2X slower than Desktop GeForce at HSR (FastMobileShaders_siggraph2011)
  Possible to prefetch textures before shading/texturing
  Hard to profile!!! ~~~Timing?
Notes: http://www.anandtech.com/show/735/3
Rather than process one polygon at a time without knowledge of other polygons in the scene, a tile based renderer first groups polygons together in groups called display lists. These display lists allow a scene to be broken into smaller blocks, known as tiles, which are then rendered independently.
The first advantage to rendering smaller portions of a scene at once is that it allows operations to be performed on-chip without having to access external memory. This allows all z-calculations to be performed without having to access an external z-buffer via the memory bus. Naturally, this eliminates the expensive z-buffer reads and writes that occur constantly on immediate mode renderers.
Rendering small tiles instead of a complete scene also means that pixels that are not visible can be thrown out before the rendering process beings. Since each tile consists of a display list that includes each polygon in that tile, hidden surface removal can occur before any textures are applied. Once again this significantly reduces the amount of information that must travel over the memory bus, as textures for non-visible surfaces do not need to be processed. Also located on chip is a tile buffer which acts as a fame buffer for an individual tile. This allows blending to be performed without costly memory reads and writ

## Slide 18: Data/texture compression
ARM’s Adaptive Scalable Texture Compression (ASTC) supported by most mobile GPU vendors
ETC2/EAC standard compression OpenGL ES 3.0
Compression hardware also present in display hardware
  Rendered images stored and transferred to the display in a compressed
    Saving bandwidth

## Slide 19: Other optimizations
Deferred shading
Primitive elimination
Skipping updates to pixels that do not change
  ARM memory transaction elimination
Notes: IMR / TBR / TBDR
http://blog.imgtec.com/powervr/understanding-powervr-series5xt-powervr-tbdr-and-architecture-efficiency-part-4
http://wenku.baidu.com/view/85ea8fec998fcc22bcd10dcb.html

## Slide 20: Trends
Specific hardware for ray tracing
Learning libraries & hardware (e.g. Qualcomm’s Fast CV, Nvidia’s CUDA Deep Neural Network)
Skipping updates to pixels that do not change
  ARM memory transaction elimination
Notes: IMR / TBR / TBDR
http://blog.imgtec.com/powervr/understanding-powervr-series5xt-powervr-tbdr-and-architecture-efficiency-part-4
http://wenku.baidu.com/view/85ea8fec998fcc22bcd10dcb.html

## Slide 21
Applications

## Slide 22: Applications
Wide range of applications
  Cultural Heritage
  Medical Image
  3D object registration
  GIS
  Gaming
  VR & AR
  Building reconstruction
  Virtual HCI
3D representation
+ additional information

## Slide 23: Mobile 3D interactive graphics
General pipeline similar to standard interactive applications
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame

## Slide 24: Remote rendering
MOBILE DEVICE
SERVER
General solution since first PDAs
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame
NETWORK

## Slide 25: Remote rendering
3D graphics applications require intensive computation and network bandwidth
  electronic games
  visualization of very complex 3D scenes
Remote rendering has long history and it is successfully applied for gaming services
  Limitation: interaction latency in cellular networks

## Slide 26: Mixed Mobile/Remote rendering
MOBILE DEVICE
SERVER
As mobile GPUs progress...
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame
NETWORK

## Slide 27: Mixed Mobile/Remote rendering
Model based versus Image based methods
Model based methods
  Original models
  Partial models
  Simplified models
    Couple of lines
    Point clouds
Eisert and Fechteler. Low delay streaming of computer graphics (ICIP 2008)
Gobbetti et al. Adaptive Quad Patches: an Adaptive Regular Structure for Web Distribution and Adaptive Rendering of 3D Models. (Web3D 2012)
Balsa et al.,. Compression-domain Seamless Multiresolution Visualization of Gigantic Meshes on Mobile Devices (Web3D 2013)
Diepstraten et al., 2004. Remote Line Rendering for Mobile Devices (CGI 2004)
Duguet and Drettakis. Flexible point-based rendering on mobile devices (IEEE Trans. on CG & Appl, 2004)

## Slide 28: Mixed Mobile/Remote rendering
Model based versus Image based methods
Model based methods
  Original models
  Partial models
  Simplified models
    Couple of lines
    Point clouds
Eisert and Fechteler. Low delay streaming of computer graphics (ICIP 2008)
Gobbetti et al. Adaptive Quad Patches: an Adaptive Regular Structure for Web Distribution and Adaptive Rendering of 3D Models. (Web3D 2012)
Balsa et al.,. Compression-domain Seamless Multiresolution Visualization of Gigantic Meshes on Mobile Devices (Web3D 2013)
Diepstraten et al., 2004. Remote Line Rendering for Mobile Devices (CGI 2004)
Duguet and Drettakis. Flexible point-based rendering on mobile devices (IEEE Trans. on CG & Appl, 2004)
Point clouds organized as hierarchical grids.
Tested on PDAs

## Slide 29: Mixed Mobile/Remote rendering
Model based versus Image based methods
Model based methods
  Original models
  Partial models
  Simplified models
    Couple of lines
    Point clouds
Eisert and Fechteler. Low delay streaming of computer graphics (ICIP 2008)
Gobbetti et al. Adaptive Quad Patches: an Adaptive Regular Structure for Web Distribution and Adaptive Rendering of 3D Models. (Web3D 2012)
Balsa et al.,. Compression-domain Seamless Multiresolution Visualization of Gigantic Meshes on Mobile Devices (Web3D 2013)
Diepstraten et al., 2004. Remote Line Rendering for Mobile Devices (CGI 2004)
Duguet and Drettakis. Flexible point-based rendering on mobile devices (IEEE Trans. on CG & Appl, 2004)
Transfer couple of 2D line primitives over the network, which are rendered locally by the mobile device

## Slide 30: Mixed Mobile/Remote rendering
Gobbetti et al. Adaptive Quad Patches: an Adaptive Regular Structure for Web Distribution and Adaptive Rendering of 3D Models. (Web3D 2012)
Balsa et al.,. Compression-domain Seamless Multiresolution Visualization of Gigantic Meshes on Mobile Devices (Web3D 2013)
Diepstraten et al., 2004. Remote Line Rendering for Mobile Devices (CGI 2004)
Duguet and Drettakis. Flexible point-based rendering on mobile devices (IEEE Trans. on CG & Appl, 2004)
Model based versus Image based methods
Model based methods
  Original models
  Partial models
  Simplified models
    Couple of lines
    Point clouds
Eisert and Fechteler. Low delay streaming of computer graphics (ICIP 2008)
Intercept and stream OpenGL commands
Better performances with respect to video streaming
Limitation: clients need powerful GPU

## Slide 31: Mixed Mobile/Remote rendering
Model based versus Image based methods
Model based methods
  Original models
  Partial models
  Simplified models
    Couple of lines
    Point clouds
Eisert and Fechteler. Low delay streaming of computer graphics (ICIP 2008)
Gobbetti et al. Adaptive Quad Patches: an Adaptive Regular Structure for Web Distribution and Adaptive Rendering of 3D Models. (Web3D 2012)
Balsa et al.,. Compression-domain Seamless Multiresolution Visualization of Gigantic Meshes on Mobile Devices (Web3D 2013)
Diepstraten et al., 2004. Remote Line Rendering for Mobile Devices (CGI 2004)
Duguet and Drettakis. Flexible point-based rendering on mobile devices (IEEE Trans. on CG & Appl, 2004)
More details in Part 5

## Slide 32: Mixed Mobile/Remote rendering
Image based methods
  Image impostors
  Environment maps
  Depth images
Noimark and Cohen-Or. Streaming scenes to mpeg-4 video-enabled devices (IEEE, CG&A 2003)
Lamberti and Sanna. A streaming-based solution for remote visualization of 3D graphics on mobile devices (IEEE, Trans. VCG, 2007)
Bouquerche and Pazzi. Remote rendering and streaming of progressive panoramas for mobile devices (ACM Multimedia 2006)
Zhu et al. Towards peer-assisted rendering in networked virtual environments (ACM Multimedia 2011)
Shi et al. A Real-Time Remote Rendering System for Interactive Mobile Graphics
(ACM Trans. On Multimedia, 2012)
Doellner et al. Server-based rendering of large 3D scenes for mobile devices using G-buffer cube maps ( ACM Web3D, 2012)

## Slide 33: Mixed Mobile/Remote rendering
Image based methods
  Image impostors
  Environment maps
  Depth images
Noimark and Cohen-Or. Streaming scenes to mpeg-4 video-enabled devices (IEEE, CG&A 2003)
Lamberti and Sanna. A streaming-based solution for remote visualization of 3D graphics on mobile devices (IEEE, Trans. VCG, 2007)
Bouquerche and Pazzi. Remote rendering and streaming of progressive panoramas for mobile devices (ACM Multimedia 2006)
Zhu et al. Towards peer-assisted rendering in networked virtual environments (ACM Multimedia 2011)
Shi et al. A Real-Time Remote Rendering System for Interactive Mobile Graphics
(ACM Trans. On Multimedia, 2012)
Doellner et al. Server-based rendering of large 3D scenes for mobile devices using G-buffer cube maps ( ACM Web3D, 2012)
Image representations are created by the server,
and warped in real time by the client to account for user interaction

## Slide 34: Mixed Mobile/Remote rendering
Model based vs Image based methods
  Constraints: rendering quality, bandwidth, interactivity
Model based
Image based
Network bandwidth
Client computation
Rendering quality
Occlusion warping limitations
Image impostors
Environment maps
Depth images
Simplified models
Partial models
Original models

## Slide 35: Mobile visualization systems
Volume rendering
Point cloud rendering
Moser and Weiskopf. Interactive volume rendering on mobile devices. Vision, Modeling, and Visualization VMV. Vol. 8. 2008.
Noguerat al. Volume Rendering Strategies on Mobile Devices. GRAPP/IVAPP. 2012.
Campoalegre, Brunet, and Navazo. Interactive visualization of medical volume models in mobile devices. Personal and ubiquitous computing 17.7 (2013): 1503-1514.
Balsa et al. Interactive exploration of gigantic point clouds on mobile devices. ( VAST 2012)
He et al. A multiresolution object space point-based rendering approach for mobile devices (AFRIGRAPH, 2007)
Rodríguez, Marcos Balsa, and Pere Pau Vázquez Alcocer. Practical Volume Rendering in Mobile Devices. Advances in Visual Computing. Springer, 2012. 708-718.

## Slide 36: Mobile visualization systems
Volume rendering
Point cloud rendering
Moser and Weiskopf. Interactive volume rendering on mobile devices. Vision, Modeling, and Visualization VMV. Vol. 8. 2008.
Noguerat al. Volume Rendering Strategies on Mobile Devices. GRAPP/IVAPP. 2012.
Campoalegre, Brunet, and Navazo. Interactive visualization of medical volume models in mobile devices. Personal and ubiquitous computing 17.7 (2013): 1503-1514.
Balsa et al. Interactive exploration of gigantic point clouds on mobile devices. ( VAST 2012)
He et al. A multiresolution object space point-based rendering approach for mobile devices (AFRIGRAPH, 2007)
Rodríguez, Marcos Balsa, and Pere Pau Vázquez Alcocer. Practical Volume Rendering in Mobile Devices. Advances in Visual Computing. Springer, 2012. 708-718.
see section 5 for details

## Slide 37: Mobile rendering
MOBILE DEVICE
Nowadays...
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame

## Slide 38: Mobile rendering
MOBILE DEVICE
SERVER
Or better...
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame
NETWORK

## Slide 39: Mobile rendering
MOBILE DEVICE
SERVER
Or better...
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame
NETWORK
Chunk-based data streaming
(like HuMoRS Balsa et al. 2014)
Limitations: bandwidth consumption (for now)

## Slide 40: Mobile rendering with capture
MOBILE DEVICE
Exploiting mobile device sensors...
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame
CAPTURE
Environment

## Slide 41: Mobile rendering with capture
MOBILE DEVICE
Exploiting mobile device sensors...
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame
CAPTURE
Environment
3D scanning with mobile phone
Kolev et al, CVPR 2014
ETH Zurich
Kolev et al. Turning Mobile Phones into 3D Scanners (CVPR 2014)
Tanskanen et al. Live Metric 3D Reconstruction on Mobile Phones (ICCV 2013)

## Slide 42: Mobile rendering with capture
MOBILE DEVICE
Exploiting mobile device sensors...
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame
CAPTURE
Environment
Example:
Google Tango
https://www.google.com/atap/projecttango/#project

## Slide 43: Mobile rendering with capture
MOBILE DEVICE
Exploiting mobile device sensors...
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame
CAPTURE
Environment
see section 4 for more
applications of sensor integration

## Slide 44: Trends in mobile graphics
Hardware acceleration for improving frame rates, resolutions and rendering quality
  Parallel pipelines
  Real-time ray tracing
  Multi-rate approaches

## Slide 45: SGRT: Real-time ray tracing
Samsung reconfigurable GPU based on Ray Tracing
Main key features:
  an area-efficient parallel pipelined traversal unit
  flexible and high-performance kernels for shading and ray generation
Lee, Won-Jong, et al. SGRT: A mobile GPU architecture for real-time ray tracing. Proceedings of the 5th High-Performance Graphics Conference, 2013.
Shin et al., Full-stream architecture for ray tracing with efficient data transmission, 2014 IEEE ISCAS

## Slide 46: Adaptive shading
Triangles rasterized into coarse fragments that correspond to multiple pixels of coverage
Coarse fragments are shaded, then partitioned into fine fragments for subsequent per-pixel shading
He et al. Extending the graphics pipeline with adaptive, multi-rate shading. ACM Transactions on Graphics (TOG) 33.4 , 2014.
Clarberg, Petrik, et al. AMFS: adaptive multi-frequency shading for future graphics processors. ACM Transactions on Graphics (TOG) 33.4 , 2014.
Won-Jong Lee, et al. Adaptive multi-rate ray sampling on mobile ray tracing GPU. In SIGGRAPH ASIA 2016 Mobile Graphics and Interactive Applications (SA '16).

## Slide 47: Mobile rendering with capture
MOBILE DEVICE
Exploiting mobile device sensors...
DATA
ACCESS
RENDERING
DISPLAY
INTERACTION
Scene
Frame
CAPTURE
Environment

## Slide 48: Examples: Physical simulations
Framework for physically and chemically-based simulations of analog alternative photographic processes
Efficient fluid simulation and manual process running on iPad
Echevarria et al. Computational simulation of alternative photographic processes. Computer Graphics Forum. Vol. 32. 2013.

## Slide 49: Examples: Correcting visual aberrations
Computational display technology that predistorts the presented content for an observer, so that the target image is perceived without the need for eyewear
Demonstrated in low-cost prototype mobile devices
Huang, Fu-Chung, et al. Eyeglasses-free display: towards correcting visual aberrations with computational light field displays.ACM Transactions on Graphics (TOG) 33.4, 2014.

## Slide 50: Conclusions
Heterogeneous applications
  driven by bandwidth and processing power
Trends
  desktop software solutions tend to be ported to the mobile world
    gaming
    modelling and 3D animation
    complex illumination models
Sensor integration open new scenarios
  examples: live acquisition, mHealth (using sensors and cameras for tracking and processing signals)

## Slide 51: Graphics development for mobile systems
Next Session