## Slide 1: Part 4
Mobile metric capture and reconstruction

## Slide 2: Computer vision and mobile applications
2010
2000
1990
Panoramic photos
(autostitch)
Digital photos
(auto enhance)
3D capture
Biometrics
(fingerprints)
Visual Search
Landmark recognition
Image Search
Face detection
VSLAM
HDR
Augmented
Reality
Material
Capture

## Slide 3: Computer vision and mobile applications
Mostly 2D
  Image enhancement
  Image stitching
  Image matching
  Object detection
  Texture classification
  Activity recognition
  …
Mostly 3D
  Camera localization
  Pose estimation
  3D shape recovery
  3D scene reconstruction
  Material/appearance recovery
  Augmented reality
  …

## Slide 4: Applications made possible by specific features of mobile devices!
Features
  Mobility
  Camera
  Active light
  Non-visual sensors
  Processing power
  Connectivity
  Display

## Slide 5: Features (1/7): Mobility
Consumer
  Smartphones
  Tablets
Embedded
  Autonomous driving
  Assistive technologies
Specific
  Drones
  Robots

## Slide 6: Features (1/7): Mobility
Consumer
  Smartphones
  Tablets
Embedded
  Autonomous driving
  Assistive technologies
Specific
  Drones
  Robots
On-site applications / Personal applications / Motion and/or location taken into account / Embedded solutions

## Slide 7: Features (2/7): High-res/flexible camera
Common features
  High resolution and good color range (>12 MP, HDR)
  Small sensors (similar to point and shoot cameras – approx. 1/3”)
  High video resolution and frame rate (4K at 30fps)
Wide variety of field of views
  standard, fisheye, spherical
Specialized embedded cameras…
  Better lenses and sensors…

## Slide 8: Features (2/7): High-res/flexible camera
Common features
  High resolution and good color range (>12 MP, HDR)
  Small sensors (similar to point and shoot cameras – approx. 1/3”)
  High video resolution and frame rate (4K at 30fps)
Wide variety of field of views
  standard, fisheye, spherical
Specialized embedded cameras…
  Better lenses and sensors…
Visual channel is the primary one
Computational photography
Apps analyze/use snapshots or videos

## Slide 9: Features (3/7): Active lighting
All smartphones have a flashlight
  LED source at fixed distance from camera
Custom devices have integrated emitters
  Google TANGO / Microsoft Kinect
    Integrated depth sensor
Leads to specialized capture procedures

## Slide 10: Features (3/7): Active lighting
All smartphones have a flashlight
  LED source at fixed distance from camera
Custom devices have integrated emitters
  Google TANGO / Microsoft Kinect
    Integrated depth sensor
Leads to specialized capture procedures
Specialized capture procedures exploiting synchronization of illumination and visual sensing
Ex. Riviere et al. Mobile surface reflectometry. Computer Graphics Forum. 2015.

## Slide 11: Features (4/7): Non-visual sensors
Absolute reference
  GPS / A-GPS
    Mainly for outdoor applications
  Magnetometer
    Enable compass implementation
    Often inaccurate for indoor
Relative reference
  Accelerometer
    Variable accuracy (sensitive to temperature)
    Good metric information for small scale scene
  Gyroscope
    Very good accuracy for device relative orientation
Synced with camera!

## Slide 12: Features (4/7): Non-visual sensors
Absolute reference
  GPS / A-GPS
    Mainly for outdoor applications
  Magnetometer
    Enable compass implementation
    Often inaccurate for indoor
Relative reference
  Accelerometer
    Variable accuracy (sensitive to temperature)
    Good metric information for small scale scene
  Gyroscope
    Very good accuracy for device relative orientation
Synced with camera!
Data fusion!
Ex. Garro et al. Fast Metric Acquisition with Mobile Devices. VMV 2016
.

## Slide 13: Features (5/7): Processing power
Growing performance of mobile CPU+GPU
  (see previous sections)
Capable to execture computer vision pipeline on mobile device
  i.e. OpenCV for Android
Some limitations due to power consumption

## Slide 14: Features (5/7): Processing power
Growing performance of mobile CPU+GPU
  (see previous sections)
Capable to execture computer vision pipeline on mobile device
  i.e. OpenCV for Android
Some limitations due to power consumption
On-board pre-processing or even full processing
Ex. Tanskanen et al. Live Metric 3D Reconstruction on Mobile Phones. ICCV2013
.

## Slide 15: Features (6/7): Connectivity
Many connectivity options
  Local area: NFC, Bluetooth, Bluetooth Low Energy, Wi-Fi 802.11x
  Wide area: Cellular wireless networks: 3G/4G/5G
Mobile devices can connect at local or wide area at reasonable speed
  Typical LTE/4G: 18 Mbps down, 9.0 Mbps up
  Typical Wi-Fi: 54Mbps (g), 300Mbps (n), 1Gbps (ac).
Lo-cost -> No-Costs
The internet; on-line
repositories
Computing nodes (back
end) (cloud, server)
Mobile system

## Slide 16: Features (6/7): Connectivity
Many connectivity options
  Local area: NFC, Bluetooth, Bluetooth Low Energy, Wi-Fi 802.11x
  Wide area: Cellular wireless networks: 3G/4G/5G
Mobile devices can connect at local or wide area at reasonable speed
  Typical LTE/4G: 18 Mbps down, 9.0 Mbps up
  Typical Wi-Fi: 54Mbps (g), 300Mbps (n), 1Gbps (ac).
Lo-cost -> No-Costs
The internet; on-line
repositories
Computing nodes (back
end) (cloud, server)
Mobile system
Load balancing (client / server)
Access to large databases (e.g., search)
Communication
Ex. Gammeter et al. Server-side object recognition and client-side object tracking for mobile augmented reality. CVPRW 2010.

## Slide 17: Features (7/7): Display!
Hi-res/hi-density display
  Data presentation!
Co-located with camera + other sensors
  Tracking during capture!
Touch screen
  Co-located user-interface
  (UI also may exploits other sensors)

## Slide 18: Features (7/7): Display!
Hi-res/hi-density display
  Data presentation!
Co-located with camera + other sensors
  Tracking during capture!
Touch screen
  Co-located user-interface
  (UI also may exploits other sensors)
Data/result presentation
Guided capture / Augmentation
Ex. Pintore et al. Mobile Mapping and Visualization of Indoor Structures to Simplify Scene Understanding and Location Awareness. ECCV ACVR 2016

## Slide 19: Wrap-up: mobile apps characterized by the exploitation of mobile device features
Features
  Mobility
  Camera
  Active light
  Non-visual sensors
  Processing power
  Connectivity
  Display

## Slide 20: Data fusion for metric capture
Example 1

## Slide 21: Metric acquisition with a commodity mobile phone
Goal
  Capture 3D models with real-world measures
Data fusion approach
  Exploit synchronization of visual sensor & IMU to capture scenes in real-world units
Garro et al. Fast Metric Acquisition with Mobile Devices. VMV 2016

## Slide 22: Structure-from-Motion + Dense reconstruction
SfM reconstructs a point cloud from a series of images
  3D positions of (sparse) matched features
  Camera positions and orientations
Many approaches for densification
  Pipeline showed to work at interactive rates on phones (Taskanen et al 2013)
SCALE AMBIGUITY

## Slide 23: Data fusion: Visual + IMU
Use sensors synced with visual channel
  GPS+Magnetometer generally not applicable
  IMU returns orientation and acceleration in real world units
Idea
  track camera movement with IMU during visual capture
  use IMU data to find out the real-world distance between SfM camera positions, resolving the scale ambiguity

## Slide 24: Data fusion: Visual + IMU
The accelerometer returns acceleration
Therefore, we should be able to compute the displacement between two camera positions as
Not so easy: onboard IMU sensors are biased and noisy and SfM camera positions are sparse

## Slide 25: Data fusion approaches (1/5)
Match position from IMU integration with position from SfM, coping with noise/bias by extensive filtering
Requires LONG acquisition times and LONG offline processing times
Visual-Inertial Navigation, Mapping and Localization:
A Scalable Real-Time Causal Approach [Jones,Soatto 2011]
Vision only
IMU only
Vision+IMU
A new approach to vision-aided inertial
navigation [Tardif et al 2010]

## Slide 26: Data fusion approaches (2/5)
Ad-hoc online solutions taking into account IMU characteristics
  Segment motion in “swift movements” with large accelerations
  Integration of IMU acceleration to derive position matched with SfM
  Continuous process of outlier rejection and re-estimation of scale
Working but motion-dependent and prone to accumulation error due to integration
Live metric 3D reconstruction on
Mobile Phones [Tanskane et al. 2013]
One estimate of λ at the end of each swift movement
Estimation of scale λ only on inlier set I

## Slide 27: Data fusion approaches (3/5)
Match accelerations from IMU with accelerations from SfM
Works off-line and assumes high-accuracy (robotics) IMU
Camera trajectory estimation using inertial measurements
and Structure from Motion results [JungTaylor2001]
spline parameters

## Slide 28: Data fusion approaches (4/5)
Match accelerations from IMU with accelerations from SfM at SfM frame-rate (large baseline!)
  Downsample and anti-alias IMU samples at SfM frame rate
  Optimize scale and bias
Requires very long acquisition times due to downsampling at SfM rate
Hand-waving away scale [Ham et al. 2014]
D: convolutional matrix for
antialising and downsampling
IMU signal

## Slide 29: Data fusion approaches (5/5)
Match accelerations from IMU with accelerations from SfM at IMU frame-rate (small baseline!)
  Upsample SfM samples at high rate using all available visual data
  Estimate acceleration from upsampled transforms and match them to IMU samples using robust fitting
Fast, coping with large errors and noise
Fast Metric Acquisition with Mobile Devices. [Garro et al. 2016}

## Slide 30: Vision Module Pipeline

## Slide 31: Vision Module
Traces Shi-Thomasi features
When baseline is large enough
  Estimate Essential Matrix, that is, relative camera pose between f0 and fi
  Calculate a 3D point for each feature point
Note: each pair of cameras has its own reference system
f0
f1
fi

## Slide 32: Vision Module
Global registration
  M point clouds
  A subset of features is present in each point cloud
  Use feature correspondence to align all the point cloud in the same reference system
Cameras upsampling
  Features are tracked for all frames
  Use aligned point cloud and tracking position to estimate cameras for all frames with Perspective-n-Point (PnP)
f0
fM
f1
fM-1
fi
2D
3D

## Slide 33: Recovering the scale factor (1/2)
IMU accelerations
Camera accelerations
Problem to solve

## Slide 34: Recovering the scale factor (2/2)
LS, gradient descent (et similia) poorly conditioned
  Not so many data
  Severe outliers
Robust fitting use RANSAC approach
  Use MLESAC robust estimator to maximize likelihood rather than just the number of inliers
Introduce rotation matrix R
  Account for orientation bias
  Improve RANSAC performance

## Slide 35: Results
Median error 4% (wrt 10-15% of other STAR solutions)

## Slide 36: Data fusion and communication for indoor capture
Example 2

## Slide 37: Indoor capture + presentation
Creation and sharing of indoor digital mock-ups
  Exploiting the capabilities of modern mobile devices
Much interest/applications (security, location awareness, …)
  Need to capture visual information together with room structure

## Slide 38: Typical solutions
Indoor capture and modeling
  Manual modeling
  Semi-automatic methods based on high-density data
    Laser scanning
      Professional but expensive, limited to specific applications
    Multi-view stereo from photographs
      Generally cost effective but hard to apply in the indoor environment
        Walls poorly textured, occlusions, clutter
        Furthermore: need for heavy MW constraints, computationally demanding
Mura et al. Piecewise-planar Reconstruction of Multi-room Interiors with Arbitrary Wall Arrangements.
Computer Graphics Forum – Pacific Graphics 2016
MVS
MWS
Merging
Furukawa et al. Reconstructing Building Interiors from Images. ICCV 2009

## Slide 39: Examples using low-cost mobile devices
Interactive capture and mapping of indoor environment
  MagicPlan - http://www.sensopia.com
    Floor corners marked via an augmented reality interface
    Manual editing of the room and floor plan merging using the screen interface
  Sankar and Seitz: Capturing indoor scenes with smartphones (UIST2012)
    Corners marked on the screen during video playback

## Slide 40: Exploiting panoramic images
360 degrees images are easy to capture using common devices
  Interactive apps using IMU + GUI + automatic stitching
  Dedicated cameras
360 degrees images are easy to navigate
  Spheremaps + emerging formats video+image formats
  VR devices for immersion
What about analyzing them?

## Slide 41: Finding the room structure
Take one spheremap per room
  Equirectangular images generated by a mobile device
    Vertical lines aligned with the gravity vector
    Image approx. oriented towards magnetic North
  Eventually use IMU + Visual features for stitching
Track user motion to identify connections between rooms
  Use IMU + Visual Features for tracking
Solve local + global optimization to find indoor structure
  Multi-room environment

## Slide 42: Finding the room structure
Analyze spheremap to extract single room structure
  Room model considers vertical walls
  Extract edges and filter out regions likely far from top/bottom edges of walls
  Find wall height
    Voting scheme used to extract most likely wall height by maximizing pairs of matching wall-floor / wall-height edge pixels
  Fit 2.5D room model to recovered wall edge map
Uses specialized transform to speed-up computation
Vary hw results in a transform scaling
TRANSFORM
SUPERPIXELS MASK
Floor
Ceiling

## Slide 43: Finding the rooms structure
Iterated to map the entire floor-plan
  Mobile tracking of user’s direction moving between adjacent rooms creates a connected room graph
  Doors position identification in the image by computer vision
  Doors matching according with graph
  Rooms displacement
  Global optimization of combined model
    Pintore et al. Omnidirectional image capture on mobile devices for fast automatic generation of 2.5D indoor maps. IEEE WACV 2016

## Slide 44: Results
Reasonable, fast reconstruction with rough structure and visual features
    Pintore et al. Omnidirectional image capture on mobile devices for fast automatic generation of 2.5D indoor maps. IEEE WACV 2016

## Slide 45: Sharing the indoor model
Indoor model
  Exploration graph
    Each node is a spheremap/room
    edges (yellow) are transitions between adjacent rooms
    Stored on a server (standard http Apache2)
  Panoramic images
    Mapped according with the graph
Interactive exploration
  Room
    WebGL fragment shader
    dragging to change view orientation and pinching to zoom in/out
  Passages
    Real-time rendering of the transitions between rooms
      Exploiting geometric model stored on the server
      Performance improvement compared to use precomputed videos
    Suggested paths

## Slide 46: Some results
Reconstruction of a 70 rooms floor of the NHV ministry at Den Haag, Netherlands. The whole model was acquired with a Ricoh Theta S camera
Live demo: http://vcg.isti.cnr.it/vasco/
Click on the dataset on the left column to start
3D reconstruction of a 655 mq office with 19 rooms.
This environment was acquired with a mobile phone
(HTC One M8)

## Slide 47: Wrap-up: mobile apps characterized by the exploitation of mobile device features
Features
  Mobility
  Camera
  Active light
  Non-visual sensors
  Processing power
  Connectivity
  Display

## Slide 48: BREAK!
After the break: rendering!